## Slide 1: Design and Technology 2020
Useful Revision Websites:
Www.technologystudent.com

## Slide 2: General Advice
When completing your design and technology exam it is always important to remember to read the questions carefully and highlight the key things.
If ever you are unsure about an answer do not panic, move past the question and then come back to it at a later point, if still unsure make a guess as you never know it could be correct. Try not to leave any answer blank if you can help it.
Don’t forget that you will need to answer every question in section A but only one question from section B – this will be on timbers.

## Slide 3: Command Words

## Slide 4: Key Dates to remember
Half term sessions
17th and 18th February 10-2
20th January – 14th Feb – AO 3 - Making
25th Feb – 6th March – Evaluation
Exam 22nd May PM

## Slide 5: Outline of Lessons
 | lesson 1 | lesson 2 | lesson 3 | homework |  | 
3rd February | NEA: Making | NEA: Making | NEA: Making | working on NEA |  | NEA
10th February | NEA: Making | (HOW TO REVISE) |  | working on NEA |  | THEORY / REVISION
Half Term | WORKSHOP available all week, computer room available 2 days () |  |  | Revision |  | 
24th February | NEA: Evaluating | NEA: Evaluating | NEA: Evaluating | working on NEA |  | 
2nd March | NEA: Evaluating | NEA: Evaluating |  |  |  | 
9th March | 1.1 New and emerging technology | 1.2 Evaluating new and emerging technologies to inform design decisions | 1.3 Energy generation storage and choosing appropriate sources |  |  | 
16th March | 1.4 Smart and composite materials and technical textiles | 1.5 Mechanical devices used to produce movement |  |  |  | 
23rd March | 1.6 Electronic Systems and 1.7 Programmable Components | CATCH UP / EXAM QUESTIONS ON CORE | 1.8 Categorisation of ferrous and non-ferrous metals |  |  | 
30th March | 1.9 papers and boards | 1.10 Thermoforming and Thermosetting Polymers |  |  |  | 
EASTER |  |  |  |  |  | 
20th April | 1.11 fabrics and fibres | 1.12 Natural and manufactured timber | 1.13 All design and technological practice takes place within contexts |  |  | 
27th April | 1.14 Challenges that influence the processes of design and making | 1.15 Investigate and analyse the work of professionals and companies to inform design |  |  |  | 
4th May | 1.16 Use of different design strategies | EXAM QU | EXAM QU |  |  | 
11th May | EXAM QU | EXAM QU |  |  |  | 

## Slide 6: What to Revise
Section A

## Slide 7: Technical Principles Design and technology and our world
The impact of new
and emerging
technologies on:
Industry
Enterprise
Sustainability
People
Culture
Society
The environment
Production techniques
Systems
The focus of this content is the impact of new and emerging technologies on the areas identified below.
The impact of new and emerging technologies on industry and enterprise:
Market pull – responding to demands from the market;
Technology push – development in materials and components, manufacturing methods;
Consumer choice – consumers wishing to own the latest technologies/products.
The Product Life Cycle.
Global production and its effects on culture and people.
Legislation to which products are subject.
Consumer rights and protection for consumers when purchasing and using products.
Moral and ethical factors related to manufacturing products and the sale and use of products.
Sustainability; meeting today’s needs without compromising the needs of future generations.
Advantages and disadvantages of using computer aided design (CAD).
Advantages and disadvantages of the use of computer aided manufacture (CAM).
How CAM equipment can be used in a variety of applications:
CNC embroidery, vinyl cutting, CNC routing, laser cutting and 3D printing.

## Slide 8
How the critical
evaluation of new and
emerging technologies
informs design
decisions; considering
contemporary and
potential future
scenarios from
different perspectives,
such as ethics and the
environment.
How energy is
generated and stored
in order to choose and
use appropriate
sources to make
products and to power
systems
The focus of this content is how the critical evaluation of new and emerging technologies informs design decisions.
The importance of sustainability issues and environmental issues when designing and making.
Social, cultural, economic and environmental responsibilities in designing and making products.
The SIX R's of sustainability; rethink, reuse, recycle, repair, reduce and refuse.
Life Cycle Analysis to determine the environmental impact of a product.
Fair-trade policies and carbon footprint.
Ecological footprint.
Types of renewable and non-renewable energy sources: wind, solar, geothermal, hydroelectric, wood/biomass, wave, coal, gas, nuclear and oil.
Issues surrounding the use of fossil fuels: coal, oil and gas.
The advantages and disadvantages of renewable energy sources.
The use of renewable energy sources in modern manufacturing production systems: the use of solar panels and wind turbines in manufacturing sites.
Renewable energy sources for products: wind-up and photovoltaic cells.
Energy generation and storage in a range of contexts: motor vehicles (e.g. petrol/diesel, electricity) and household products (e.g. battery, solar, mains electricity)

## Slide 9
Smart materials, composites and technical textiles
Developments in
modern and smart
materials, composite
materials and
technical textiles.
Electroluminescent film or wire i.e. LCD.
Quantum Tunnelling Composite (QTC) - when used in circuits the resistance changes under compression.
SMA – shape memory alloys.
Polymorph.
Smart fibres and fabrics that respond to the environment or stimuli:
Photo-chromic;
Thermo-chromic;
Micro-encapsulation;
Biometrics.
Carbon Fibre, Kevlar and GRP.
Interactive textiles that function as electronic devices and sensors: circuits integrated into fabrics, such as heart rate monitors; wearable electronics such as mobile phones or music player, GPS, tracking systems and electronics integrated into the fabric itself.
Micro-fibres in clothing manufacture.
Phase changing materials: breathable materials; proactive heat and moisture management.
Sun protective clothing.
Nomex.
Geotextiles for landscaping.
Rhovyl as an antibacterial fibre.

## Slide 10
Electronic systems and programmable components
How electronic
systems provide
functionality to
products and
processes, including
sensors and control
devices to respond to
a variety of inputs, and
devices to produce a
range of outputs
Graphical conventions for communicating concepts: circuit diagrams, block diagrams and flowcharts.
The ‘systems' approach – input; process; output.
Principles of a control system:
Input data from a sensor: light dependent resistor (LDR),
thermistor;
Processing by control devices: semi-conductor, IC,
microprocessor or computer;
Output where a signal is received that will perform a desired
function: buzzer, light emitting diode (LED).
The importance of feedback within the system.
The methods of providing feedback in different systems.
Familiar products in terms of their control system.
Control devices that include counting, switching and timing.
Analogue and digital sensors as input components.

## Slide 11
The use of
programmable
components to embed
functionality into
products in order to
enhance and
customise their
operation
Sub routines or macros in control systems.
Programmable microcontrollers can be used to control a rangeof systems.
Programmable microcontrollers can interface with other devices.
Programmable microcontrollers can be reprogrammed
repeatedly.
The benefits and limitations of programmable microcontrollers.
Programmable Interface Controllers (PIC) and how they can be used to control products or systems.

## Slide 12
Mechanical components and devices
The functions of
mechanical devices,
to produce different
sorts of movement,
changing the
magnitude and
direction of forces.
Principle of a mechanical device to transform input motion and force into a desired output motion and force.
Analyse everyday mechanical devices and how they function.
Consider mechanical systems in terms of input; process; output.
Mechanical systems which:
increase or decrease speed of movement/rotation;
change magnitude/direction of force/ movement/ rotation.
Simple calculations involving mechanical systems.
Analyse the function of mechanical products that have:
pulley systems, e.g. curtain rails, sewing machine;
gear systems, e.g. whisk, hand drill;
levers and linkages, e.g. scissors;
rack and pinion, e.g. chair lift;
cams, e.g. automata toys.

## Slide 13
Materials
Papers and boards
The categorisation and properties of paper, cards, boards and composite materials. Properties to be considered in terms of their strength, folding ability, surface finish and absorbency.
Papers, cards and boards can be laminated to improve
strength, finish and appearance.
The standard ISO sizes of paper.
The use of grammage i.e. grams per square metre (gsm) to measure weight of paper.
The use of microns to measure thickness of card.
The use of recycled materials to manufacture papers and
boards.
The aesthetic and functional properties of common papers, cards and boards: layout paper, tracing paper, copier paper, recycled paper, corrugated board, cartridge paper, mounting board and folding boxboard.

## Slide 14
Natural and
manufactured timber
The categorisation and properties of hardwoods and softwoods.
Properties to be considered: strength, grain structure, surface finish and absorbency.
Natural timber is harvested from deciduous (hardwoods) and coniferous (softwood) trees.
Natural timber is available in the following forms: plank, board, strip, square, and dowel.
Natural timber can be identified using a range of discriminators: weight, colour, grain, texture, durability and ease of working.
Natural timber is protected using different finishes and these finishes are sometimes used to improve aesthetic appeal.
Categorisation and properties of manufactured timbers.
Manufactured timbers are made from natural timbers and made from particles/fibres or laminates.
Manufactured timbers are available in standard sizes and
forms: plywood, MDF (Medium Density Fibreboard), chipboard, hardboard and veneered boards.
Manufactured timbers can be protected using finishes and these finishes are sometimes used to improve the aesthetic appeal.

## Slide 15
Ferrous and nonferrous
metals
Categorisation and working properties of ferrous metals, nonferrous metals and alloys.
Properties of metals: hardness, elasticity, conductivity,
toughness, ductility, tensile strength and malleability.
Metals are sold as sheet, bar, rod, tube and angle.
Ferrous metals: cast iron, mild steel, medium carbon steel and high carbon steel.
Ferrous metals may require a protective finish and the finish is sometimes used to improve the aesthetic appeal.
Non-ferrous metals: aluminium, copper, brass, bronze.
Alloys of metals are a base metal mixed with other metals or non-metals to change their properties or appearance.
Non-ferrous metals may require a protective finish and the finish is sometimes used to improve the aesthetic appeal.

## Slide 16
Thermoforming
and thermosetting
polymers
Categorisation and physical properties of polymers.
Polymers can be made from both natural and synthetic
resources.
Polymers are sold as sheet, film, bar, rod and tube.
The differences between a thermoforming (thermoplastic) and thermosetting material.
Properties of polymers: weight, hardness, elasticity,
conductivity/insulation, toughness and strength.
The properties of thermoplastics: polythene, polystyrene,
polypropylene and PVC.
The properties of the thermosetting plastics: UF (urea
formaldehyde), MF (melamine formaldehyde), PR (polyester resin) and ER (epoxy resin).

## Slide 17
Natural, synthetic,
blended and mixed
fibres, and woven,
non-woven and
knitted textiles.
The categorisation and working properties of fibres and textiles.
The raw materials of textiles are classified according to their source.
Natural polymers:
Animal polymers: wool/fleece – mohair, cashmere, angora, alpaca, camel (hair).
Insect polymers: silk.
Plant polymers: cotton, linen hemp, jute, rayon, viscose.
Manufactured polymers:
Synthetic: polyester, polypropylene, nylon, acrylic, elastane, lycra, aramid fibres.
Microfibres – Tactel, Tencel (Lyocell).
The properties of textiles fibres: strength, elasticity, absorbency, durability, insulation, flammability, water-repellence, anti-static and resistance to acid, bleach and sunlight.
Blending and mixing fibres improves the properties and uses of
yarns and materials.

## Slide 18: What to Revise
Section B

## Slide 19: Natural and Manufactured Timber
The sources,
origins, physical and
working properties of
the material categories
or the components and
systems, and their
ecological and social
footprint
The physical and working properties of hardwoods,
softwoods and man-made boards: toughness, flexibility,
grain structure, strength, absorbency, surface finish, colour and hardness.
Natural solid timber - strengths and weaknesses
Defects: shrinkage, splits, shakes, knots, fungial attack.
Hardwoods: beech, oak, mahogany, balsa and jelutong.
Softwoods: scots pine, western red cedar and parana pine.
Strengths, weaknesses of the following manufactured
boards: plywood, MDF - medium density fibreboard, chipboard and hardboard.
The impact on the environment of deforestation.
Ecological and social footprint.
Changing society’s view on waste, encourage recycling.
Living in a greener world.
Life-cycle analysis of a material or product.

## Slide 20
The way in which
the selection of
materials or
components is
influenced by a range
of factors, such as
functional, aesthetic,
environmental,
availability, cost,
social, cultural and
ethical
Aesthetic properties of natural and manufactured timbers.
Functional properties of natural and manufactured
timbers.
Responsibilities of designers and manufacturers who
design using timber with respect to:
the environment;
working conditions in third world countries, low labour
costs and poverty;
exploitation of employees;
recyclability and waste.
Biodiversity and deforestation.
Estimating the true costs of a prototype or product.
Comparison costs of hardwoods, softwoods and
manufactured board.
The impact of forces
and stresses on
materials and objects
and the ways in which
materials can be
reinforced and
stiffened
The behaviour of natural and manufactured timber under forces or under stress.
The stiffness and a strength of natural timber will depend upon the wood, the cross sectional area and the depth of the section.
Reinforcement of natural timber by laminating.
The strength of plywood will depend upon the number of
layers and the wood grain being at right angles.
The strength of a timber product will depend upon how
the product is jointed or what fixing method is used.

## Slide 21
Stock forms, types
and sizes in order to
calculate and
determine the quantity
of materials or
components required
Natural timber is available in different sectional forms,
various standard sizes and can have a different finish
(sawn or planed).
Manufactured boards are commonly available in sheet form and in standard sizes and various thicknesses.
Calculate the costs involved in the design of products:
fixtures, fittings, finishes required and the material cost.
Alternative
processes that can be
used to manufacture
products to different
scales of production
Advantages and disadvantages of producing single, one off products.
The advantages and disadvantages of producing products
in limited quantities (batch production).
The need to produce a number of identical products.
Jigs and devices to control repeat activities.
The advantages and disadvantages of high volume,
continuous production.
Issues related to high volume production.
The importance of CAM in modern high volume production.

## Slide 22
Specialist
techniques and
processes that can be
used to shape,
fabricate, construct
and assemble a high
quality prototype,
including techniques
such as wastage,
addition, deforming
and reforming, as
appropriate to the
materials and/or
components being
used
Wastage/Addition
Tools and equipment to mark out, hold, cut, shape,
drill and form laminates of natural timbers and
manufactured boards.
The pillar drill to drill holes to various diameters.
Jigs and formers to ensure accuracy as part of the
process of drilling, bending, cutting wood materials.
Deforming/Reforming
Material joining can be permanent or temporary.
The principles of producing wood products using the
following processes: jointing, veneering, laminating
and steam bending.
Classification of wood joints as frame or box
construction.
Frame: mitre, dowel, mortise and tenon, halving and
bridle joint.
Box/carcass: butt, lap, housing, dovetail and comb
joint.
Adhesives: PVA (wood to wood), contact adhesive and
epoxy resin (wood to other materials).
Temporary: screw (countersunk and round head) and
knock down fittings.
Lasers.
CAM machines.
Appropriate surface
treatments and finishes
that can be applied for
functional and
aesthetic purposes
Surface treatments of natural timber and manufactured
boards to prolong life of a product: sealants and primers.
Finishes for aesthetic or functional reasons: varnish, wood stains, oils, polishes and preservative paints.